## Slide 1
Home Automation using
NodeMCU
Gaurav Kumar
1701CS21

## Slide 2
Overview
KEY PRESENTATION POINTS
  Introduction
  Project Aim
  What inspired this project
  Description of Project
  Hardware and Software requirements
  Design and Implementation

## Slide 3
Home Automation
Controlling Home devices from central control point.
Home automation system is getting popular and widely used in a lot of houses worldwide. It has tons of advantages to users even more to the handicapped and/or elderly users in which it will make it easier for them to control their home appliances

## Slide 4
Project Aim
The aim of the project is to design a home automation system that will remotely switch on/off any household appliances connected to it, using an app or through Google assistant with the help of NodeMCU using WiFi connectivity

## Slide 5
What inspired this project
Besides the convenience of being able to remotely control the home appliances like we can turn our a.c. on before getting home so as to have our room temp. lowered after the day's work and also being energy efficient. Remote monitoring can put our mind at ease while we’re away from the house. With remote dashboards, lights and lamps can be turned on and off, and automated blinds can be raised and lowered. These capabilities can help to mitigate the risks of intrusions

## Slide 6
  NodeMCU based home automation using WiFi helps the user to control any home appliances using app on the phone or by using voice command through Google assistant app on their android smartphone
  The Android add (Blynk) sends command to the microcontroller - NodeMCU, through WiFi . This NodeMCU is connected to the Relay board
  Relay Board has several relays which can be connected to different home appliances
  User can switch on/off these appliances using the Blynk app which is programmed as per the need - how many appliances you want to control or the initial state of appliances when we start home automation system or the specific buttons for given appliances
  User can also use Google assistant to control appliances through his/her assigned voice command
Project Description

## Slide 7
Hardware
requirements
  NodeMCU - ESP8266 wifi development board
  Relay Board(4 relay or 8 relay or even single relay may work depending on no. of appliances)
  Breadboard (may or may not be used)
  Breadboard Power supply / power bank/ battery (for power supply to the relay and NodeMCU)
  Jumper Wires
  Light bulb
  Wires

## Slide 8
Software
requirements
  Blynk app - Android/ ios
  Arduino IDE - Windows/ Linux/ Mac-os

## Slide 9
Design Procedure
  Configuring Blynk App
  Using Arduino IDE
  Hardware Assembly
  Using IFTTT

## Slide 10
Configuring
Blynk App
  We open the app and create a New Project
  After giving Project Name, select hardware device as NodeMCU and connection type as Wifi
  Blynk app will send Auth token after creating project that will be used in the code which will be uploaded to the NodeMCU
  Depending upon how many appliances we want to control we will add that many number of buttons on the blank area from the side menu
  After clicking the button we can configure the button, set its name, set it to specific input on relay, its initial state when power is supplied to nodemcu

## Slide 11
Using Arduino-IDE
  After installing and configuring Arduino-IDE we will connect NodeMCU to our pc using USB cable
  After starting the Arduino-IDE we will select appropriate port to which NodeMCU is connected to our pc under tools
  Change the board under tools to be NodeMCU 1.0
  Now, we will write the code or use the ESP8266_Standalone sample under Examples
  Set the auth token to the one that was mailed during creating project in Blynk app
  Set the network and password of wifi to which NodeMCU will connect
  Now, we upload the code and next time NodeMCU powers up it will automatically get connected to the specified network

## Slide 12
Hardware Assembly
  Connect NodeMCU to Relay Board. We can directly connect them using jumper wires or use Breadboard for this
  NodeMCU has many input pins, we can connect IN1, IN2 ... depending on how many appliances we need to connect, of relay to anyone of those but we need to configure our buttons in Blynk app accordingly
  Connect ground pin of relay to GND of nodemcu, Vcc of relay to 3v3 of nodemcu, jdvcc of relay to vin of nodemcu
  Power up NodeMCU using charger/ powerbank
  To power up Relay board we can use battery or breadboard power supply or can just use power supply from nodemcu

## Slide 13
Using IFTTT
  We cannot connect the Google Assistant to the NodeMCU directly, and that is the reason we use the Blynk app. Blynk app can directly connect to the NodeMCU and send data to it
  To send the on or off signals using voice commands. To do this we use google assistant in our smartphone and an app called IFTTT
  When we say a voice command to the Google Assistant, Google Assistant sends this command to IFTTT. IFTTT interprets this command and sends an On or Off signal to the Blynk app via the Blynk Server. Blynk will then send this signal to the NodeMCU and then to our electrical appliances
  We have to go to the IFTTT website and create and applet that accomplishes this task for us where we set the voice command given to the google assistant app and the action related to it

## Slide 14
SECURITY
ENERGY EFFICIENT
SAVINGS
CONVENIENCE
Pros

## Slide 15
INSTALLATION
SYSTEM COMPATIBILITY
COST
COMPLEX TECHNOLOGY
CONS